## Slide 1: Text Display & Keyboard Programming
CSE 214
Sabbir Ahmad | Dept. of CSE, BUET

## Slide 2: Video Adapters
Circuit that controls display on the monitor
Usually an add-in card, has two basic units
  Display Memory (Video buffer)
  Video Controller
Display Memory
  Stores information to be displayed. Accessed by CPU and video controller
  Memory address stars at segment A000h and above
Video Controller
  Reads display memory and generates appropriate signals depending on different issues.

## Slide 3: Display Modes
Computer uses different techniques and memory requirement to display text and graphics
So there are two display modes
  Text Mode
  Graphics Mode

## Slide 4: Text Mode
Screen is divided into columns and rows
  Typically 80 columns by 25 rows
  Character is displayed at each screen position
Character generation
  Created form a dot array called a “character cell”
  Adapter uses a character generator circuit to create dot patterns
  Number of dots in a cell depends on adapter resolution
  Monitor has also resolution, monitor needs to be compatible with adapter

## Slide 5: Graphics Mode
Screen divided into columns and rows but,
  Each position is called a pixel
  Picture can be displayed by specifying the color of each pixel
  Details in chapter 16

## Slide 6: Kinds of Video Adapters
MDA
  Monochrome Display Adapter (text only)
CGA
  Color Graphics Adapter (color in text and graphics 8x8)
EGA
  Enhanced Graphics Adapter (8x14 dots)
VGA
  Video Graphics Array (8x19 dots)
MCGA
  Multi-color Graphics Array (8x19 dots)

## Slide 7: Text Mode Programming
80 columns by 25 rows
A position on the screen: (column, row)
Upper left corner coordinate: (0, 0)
(0-24) rows and (0-79) columns
Character in each screen position is specified by the contents of a “word” in the display memory
“Word” for specifying a character:
  Low byte: ASCII code
  High byte: Attribute (color, blink,… ...)

## Slide 8: Display Pages
  Adapter’s display memory is divided into display pages
  One page holds data for one screen
  Page number starts form 0
  Number of pages depends on adapter
  If more than one page is available, program can display one page while updating another one
See table from book for details

## Slide 9: Display Pages
In 80x25 text mode, each display page is 4KB
MDA has only one page: page 0. It starts at location B000:0000h
CGA has 4 pages, starting address B800:0000h

## Slide 10: Active Display Page
Page that is currently being displayed
For 80x25 text mode:
  Memory requirement = 80*25 = 2000 words = 4000 bytes
  So, display doesn’t use all the 4KB (4096 bytes) in the page
Active display page is displayed on the screen row by row
Can be considered as a 2D-array stored in row-major order

## Slide 11: Attribute Byte
High byte of the word that specifies a display character
It describes:
  The color
  Intensity
  Background color
  Blinking
  Underline

## Slide 12: 16-Color Display
4 modes of operation (modes 0-3)
A “1” in bit position of attribute byte selects the attribute
  Bits: 0-2, color of the character (210-RGB)
  Bit: 3, intensity
  Bits: 4-6, background color (654-RGB)
  Bit: 7, blink
See examples form book!
See additive color wheel!

## Slide 13: Monochrome Display
Normal Video: white character on black background
Reverse Video: black character on white background
In monochrome, character can be underlined.
  01h: normal underline
  09h: bright underline

## Slide 14: INT 10h
We can display data by moving directly into active display page
For simplicity we use INT 10h: BIOS video screen routine
Video function is selected putting a function number in AH register
Lots of example: See from book!

## Slide 15: The Keyboard
Types of key
  ASCII keys
  Shift keys
  Function keys

## Slide 16: Scan Code
Each key on keyboard is assigned a unique number
When a key is pressed, keyboard circuit sends the corresponding code to computer – scan code
Also known as Make code
But how to determine Combination of keys!
Or Release of a key!

## Slide 17: Break Code
When a key is released, keyboard circuit sends another code – break code
Break code is derived form scan code by changing the MSB to 1
Computer doesn’t save information on every key pressed or released
  Only for function keys, INS, shift keys
  Information saved as individual bits called keyboard flags stored in the byte 0040:0017

## Slide 18: Keyboard Buffer
15 word block of memory queue
To store keys that are typed but not used by the program
Each keystroke stores as a word
  High byte: scan code
  Low byte: ASCII code for ASCII key, 0 for function keys
Shift, Ctrl, Alt keys are not stored in the buffer
If a key input is requested and the buffer is empty, the system waits until a key is pressed

## Slide 19: Keyboard Operation
Keyboard sends a request (interrupt 9) to computer
ISR for interrupt #9 obtains scan code, stores it in a word in the keyboard buffer
INT 21h, function 1 -> reads the ASCII code and shows on the screen
Use INT 16h, function 0 to get information from buffer
  If buffer is empty, wait for a key press
  Character is not shown on screen

## Slide 20
END