## Slide 1: Interrupts
CSE 214
Sabbir Ahmad | Dept. of CSE, BUET

## Slide 2: What is “Interrupt”?
Suspend the execution of running program, and execute another program to fulfill specific requirement upon request
After finishing the “requested program”, automatically return to the first program, at the same point from where it was left

## Slide 3: Why Interrupt!!
Is it good?
Is it must? Is it necessary?

## Slide 4: 8086 Interrupts
Hardware Interrupts
  External signal applied to NMI or INTR pin
  Checks for interrupt after executing each instruction
  Interrupt acknowledge and interrupt number to detect interrupt device
Software Interrupts
  Program calls interrupt routine using INT (don’t we know it already?)
  INT interrupt_number
Processor Exception
  Divide by zero!!
  Each exception has type or number

## Slide 5: Interrupt Service Routine (ISR)
  Written instructions of a specific interrupt service
  On an interrupt, program execution needs to jump to the interrupt service routine
  But! How to find, where the “Interrupt Routine” is?

## Slide 6: BIOS and DOS Interrupt
BIOS Interrupt
  Low level system interrupt
  Saved in the ROM
  Provided by device manufacturer for hardware device service
DOS Interrupt
  High level system interrupt
  Loaded into memory when machine starts

## Slide 7: Interrupt Number
Unsigned byte value
So, how many possible interrupt types?
  Easy!!
Not every interrupt number has interrupt service routine
  0h-1Fh for BIOS interrupts
  20h-3Fh for DOS interrupts
  Reserved numbers
  … (see complete list form book!) No need to memorise!

## Slide 8: Interrupt Number
How to get ISR address?
  Not generated directly from interrupt number
WHY?
  It would produce exact same address for every number in each machine!!
  SO? What’s the big deal?
ISR address
  Interrupt number is used to calculate an address of a memory location, where ISR is saved
  So, ISR can be anywhere in the memory, but its addresses are saved in a predefined location
  Each address is called “Interrupt Vector”!

## Slide 9: Interrupt Vector Table (IVT)
  All interrupt vectors are placed in an IVT
  Occupies the first 1KB of memory
  Interrupt vector is given as segment:offset
  Each interrupt vector is of 4 bytes! HOW?
  So, first 4 bytes denotes Interrupt Vector 0
  See figure 15.1 from book!

## Slide 10: Find ISR
What we need
  Interrupt Number
  And nothing!!
Process
  Multiply interrupt number by 4
  Gives memory location containing offset of ISR
  Segment address is in the next 2 bytes
  offset = Int_Num * 4
  Segment = offset + 2h

## Slide 11: Total Picture!
  Step 1: Saves Flag register on the stack
  Step 2: Clear IF and TF Flag. WHY?
  Step 3: Saves current CS and IP in the stack. WHY?
  Step 4: Uses Interrupt number to go to IVT
  Step 5: Loads CS and IP from specific IV
  Step 6: Jumps to specific ISR
  Step 7: Executes Interrupt Service
  Step 8: On completion, executes IRET instruction, which restores CS, IP and Flag register
  We used RET instruction! Different from IRET?

## Slide 12: Why Clear IF and TF?
IF
  IF set means, hardware devices can interrupt 8086
  This is called, “masking out external interrupts”
  There’s an Exception! (:@ why!!!)
    Called NMI (Non Maskable Interrupt) – can’t be masked out
TF
  When TF is set, 8086 generates processor exception
  Interrupt type 1. Used for DEBUG in T(trace) command
  DEBUG sets TF, then transfers control to processor
  After instruction is executed, processor generates interrupt type 1.

## Slide 13: BIOS Interrupts
INT 0h: Divide Overflow
INT 2h: NMI
INT 9h: Keyboard
INT 10h: Video
… ... ... and lots of... lots...

## Slide 14: DOS Interrupts
INT 21h: Function Request
… ... and lots of...

## Slide 15: User Interrupt Procedure
Three steps:
  Save the current interrupt vector (AH=25h)
  Place the vector of the user procedure (AH=35h)
  Restore the previous vector before termination
OFFSET & SEG pseudo-ops
  - To get offset and segment of a procedure

## Slide 16
END