## Slide 1: Color Graphics
CSE 214
Sabbir Ahmad | Dept. of CSE, BUET

## Slide 2: Graphics
Screen display is divided into columns and rows
Each position is called a pixel
Pixel
  Specified by column and row
  Columns: numbered form left to right starting with 0
  Rows: form top to bottom staring with 0
  Pixel may contain one or more dots (depends on mapping of rows and columns into scan line)
APA (all points addressable) graphics mode if a pixel is mapped to only one dot

## Slide 3: Graphics Mode
Normally set to text mode
For color graphics, first set the graphics mode
Example:
  AH = 0h
  AL = 06h
  INT 10h

## Slide 4: CGA Graphics
Three resolutions
  low: 160x100
  Medium: 320x200
  High: 640x200
BIOS INT 10h only supports medium and high resolutions
16KB of display memory located in segment B800h
Each pixel is represented by one or more bits
  High resolution: 1 bit for 1 pixel
  Medium resolution: 2 bits for 1 pixel

## Slide 5: CGA: Medium Resolution
Can display 16 colors
Four colors can be displayed at one time because of limited size of display memory
Resolution 320*200 = 64000 pixels
So, memory requirement=64000*2 bits = 16000 bytes
Palettes:
  Set of colors that can be displayed at the same time
  Each contains 3 fixed colors and a background color to be selected form 16 colors
  Background color is the default color of all pixels
  See example from book!

## Slide 6: CGA: High Resolution
Can display two colors
Pixel is 0 or 1. o for black, 1 for white
Possible to select background color
  If selected, then 0 pixel value is background color
  Pixel value 1 is white
See example from book!

## Slide 7: Writing Directly to Memory
For fast screen update, bypass BIOS routines and write directly to display memory
16 KB memory is divided into two halves
  Pixels in even numbered rows in first 8KB
  Pixels in odd numbered rows in second 8KB
  Each row is represented by 50 bytes
Before write a pixel value, we must read the byte! WHY?

## Slide 8: Displaying Text in Graphics
Not generated from character generator circuits
Characters are selected from character fonts stored in memory
In 320*200 resolution, there are 40 text columns
See example from book!

## Slide 9: EGA Graphics
ECD (enhanced color display) monitor needed
16 palette registers
16 color at the same time out of 64 colors
Can emulate CGA graphics
EGA uses four modules of 64KB each, called bit planes
So, total of 256KB
8086 cannot directly access bit planes, must go through EGA registers
8 display pages

## Slide 10: VGA Graphics
640*480 resolution
Can generate 64 levels of R, G, B
64^3=256K different colors
256 colors can be displayed at a time
Needs an analog monitor
Can emulate CGA and EGA modes

## Slide 11
END